## Slide 1: CG 3207 Design of a MIPS processor
Group 42:
Haider Hayee
Hunar Khanna
Omer Iqbal

## Slide 2: FEATURES
Operations | 
Arithmetic Operations | ADD, ADDI, SUB
Mult/Div related Operations | DIV, DIVU, MULT, MULTU, MFHI, MFLO
Logic Operations | AND, NOR, OR, ORI, XOR
Shift Operations | SLL, SRA, SRL, SLLV, SRAV, SRLV
Comparison Instructions | SLT, SLTI
Load/Store Instructions | LUI, LW, SW
Branch Instructions | BEQ, BGEZ, BGEZAL
Jump Instructions | J, JAL, JR, JALR

## Slide 3: SPECIAL FEATURES
Pipelining implementation
Data Hazard detection and forwarding in hardware
Resources optimization
Exhaustive unit and integration testing
Synthesizes on FPGA ;)

## Slide 4: Specifications
RAM Size : 16 words
ROM Size : 64 words
FPGA utilization Percentage : 91 % slices used
Clock Max frequency: 21.7 MHz
All instructions take 5 clock cycles except Div family which takes 32 clock cycles, however due to pipelining, it averages to 1 clock cycle per instruction

## Slide 5: Optimizing Utilization
All memory units (Register File, ROM, RAM) are synthesized as RAMS on the FPGA.
RAM is implemented as 4 separate 8 bit columns, allowing byte level access if needed.
Division clock cycles increased to synthesize fewer resources.
Data Hazard Logic re-implemented THREE times to reduce utilization.

## Slide 6: TESTING
Unit testing each module
Special programs implemented for integration and black box testing, like 16 bit calculator for R-type instructions, a comparator for Branch instructions etc.
Python script for automatic generation of VHDL code for ROM Data from Hex dumps.
EXTENSIVE usage of version control (git)

## Slide 7: NOT WORKING
Hardware hazard detection for BEQ, JR & friends not implemented due to time constraints . These instructions require ASM code to insert appropriate NOPs
Exception handling.

## Slide 8: Lessons Learnt
Everything :D
Thinking like hardware
Optimization strategies